## Slide 1: Pollution Prevention Partnership
Reducing ground level ozone in Nueces and San Patricio counties since 1995

## Slide 2: Why Care About Air Pollution?
Ecology
Health
Economy
Major Toxic Pollutants in Vehicle Exhaust:
  VOC— Volatile Organic Compounds, ingredients for ozone
      Unburned Fuels in Exhaust, Evaporated Fuels and Solvents
  NOx—Oxides of Nitrogen, ingredient for ozone
  PM—Particulate Matter, lodges in the lungs
  CO—Carbon Monoxide, a colorless, odorless, poisonous gas
  HCHO—Formaldehyde, a lung irritant and carcinogen
Some Economic Costs of EPA Non-Attainment
(Ozone averages >70 ppb Oct. 2015)
  Possible loss of industry and economic development
  Possible loss of federal highway and transit funding
  Restrictive permitting requirements not applied in attainment areas
  Technical and Formula Changes for product manufacturing
Notes: Pick a reason !

## Slide 3: Sources of Primary Pollutants
From EPA brochure OZONE

## Slide 4: Focus on Ozone
Ozone Good Up High
Ozone Bad Nearby

## Slide 5: Ground Level Ozone Formation
NOX
Oxides of Nitrogen
UV
Sunlight
Ozone
VOC
Volatile Organic Compounds
Corpus Christi Region Ozone Season:
April 1 to October 31
VOC’s - Unburned Fuels in Exhaust, Evaporated Fuels, Solvents and

## Slide 6: Health Effects
Most at Risk
Children
Adults who are active outdoors.
People with respiratory diseases, such as asthma
People with unusual susceptibility to ozone
Difficulty breathing deeply and vigorously
Shortness of breath and pain when taking deep breaths
Coughing and sore or scratchy throat
Inflammation and damaged airways
Aggravated lung diseases: asthma, emphysema, and chronic bronchitis.
Increased the frequency of asthma attacks.
Lungs more susceptible to infection.
Continued lung damage even when the symptoms have disappeared.
With airway inflammation, there is an influx of white blood cells, increased mucous production, and fluid accumulation and retention. This causes the death and shedding of cells that line the airways and has been compared to the skin caused by sunburn.
http://www3.epa.gov/ozonepollution/health.html

## Slide 7: The Fix
Reduce Emissions!
Find and Fix Gross Polluters
Reduce Normal Emissions
Change Habits
Alternative Fuels
Emission Controls
High MPG Vehicles
Ozone Actions
Cycling, walking
Mass transit
Carpool
Combine trips
Check
Fix
Maintain

## Slide 8: Alternative Fuels: Moving Forward
Choosing a Fuel Technology for Health, Ecology and Economy

## Slide 9: Common Alternative Fuel Vehicles (AFV)
CNG- Compressed Natural Gas
E85- 85% ethanol and 15% gasoline
LPG- Propane
HEV-Gasoline Hybrid Electric Vehicle
PHEV- Gasoline Plug-in Hybrid Electric Vehicle
EREV- Gasoline Extended Range Electric Vehicle
EV- All Electric Vehicle
https://www.fueleconomy.gov/feg/Find.do?action=sbs&id=34918
2016 Chevrolet VOLT - electric vehicle with gasoline powered range-extending capability (EREV).
Notes: Hybrids are not designed to travel extended distances in electric-only mode. Hybrids generally use battery power while stopped or at low speeds, and also cannot typically operate at high speeds while being powered by electricity alone.
EREV (Volt) is designed to travel longer distances and at all speeds (up to 100 mph on a test track) in EV mode. Once the battery is depleted, Volt uses the gas-powered, range-extending generator to drive hundreds of miles more.

## Slide 10
http://www.afdc.energy.gov/locator/stations/

## Slide 11
http://www.afdc.energy.gov/fuels/prices.html
July-1-2015

## Slide 12
http://afdc.energy.gov/data/10303

## Slide 13
http://afdc.energy.gov/data/10301

## Slide 14: Emissions Charts
Pollution Comparison by Fuel Technology

## Slide 15
Chart: Annual Pounds of NOX & Total VOC 1 Passenger Car
| Gasoline | Diesel | LPG | E85 | CNG | Gasoline HEV | Gasoline PHEV | Gasoline EREV | EV
NOx | 2.3 | 3.1 | 2.4 | 1.5 | 1.9 | 1.5 | 1.3 | 0.5 | 0
Total VOC | 3.1 | 1.1 | 3.3 | 2.9 | 1.8 | 2.4 | 2.2 | 0.7 | 0

## Slide 16
Chart: Annual Pounds of NOX & Total VOC 1 Passenger Truck
| Gasoline | Diesel | LPG | E85 | CNG | Gasoline HEV | Gasoline PHEV | Gasoline EREV (plugin) | EV
NOx | 5.7718 | 22.0516 | 5.9819 | 3.7773 | 4.8252 | 3.7181 | 3.3573 | 0.90371 | 0
Total VOC | 3.5535 | 1.2746 | 3.8349 | 3.2251 | 1.9732 | 2.8202 | 2.5465 | 0.68546 | 0

## Slide 17: Local Vehicle Stock
Nueces and San Patricio Counties (CY 2014)

## Slide 18
Chart: Passenger Cars by Fuel Type
| Gasoline ICE Vehicles | Ethanol-Flex Fuel ICE | Gasoline(HEV) | TDI Diesel ICE | PHEV | Natural Gas | All Electric | Propane
 | 175621.1771 | 4293.406 | 4044.4452 | 1893.5364 | 261.0219 | 146 | 121.4319 | 95.7693
Total count 186,477

## Slide 19
Chart: Passenger Trucks/SUV by Fuel Type
| Gasoline ICE Vehicles | Ethanol-Flex Fuel ICE | Propane | Gasoline(HEV) | TDI Diesel | Natural Gas | All Electric | PHEV
 | 86656.4137 | 10474.7245 | 495.204 | 426.6206 | 226.833 | 202.9142 | 14.288 | 0

## Slide 20
Chart: % Change from Conventional Fuel Passenger Vehicles to Alternative Fuel: NOX Reductions
| 5% Change | 10% Change | 15% Change | 20% Change | 25% Change | 30% Change
CNG | -0.0084025 | -0.016805 | -0.025207 | -0.03361 | -0.042012 | -0.050415
E85 | -0.017705 | -0.03541 | -0.053115 | -0.070819 | -0.088524 | -0.10623
HEV | -0.037037 | -0.074073 | -0.11111 | -0.14815 | -0.18518 | -0.22222
EV | -0.05 | -0.1 | -0.15 | -0.2 | -0.25 | -0.3

## Slide 21
Chart: Possible Annual Pounds of NOx Reduced With % Change from Gasoline to Alternative Fuels
| 5% Change | 10% Change | 15% Change | 20% Change | 25% Change | 30% Change
CNG | -8181.2868 | -16362.5737 | -24543.8605 | -32725.1473 | -40906.4342 | -49087.721
E85 | -17238.8038 | -34477.6076 | -51716.4114 | -68955.2152 | -86194.0189 | -103432.8227
HEV | -36061.7533 | -72123.5065 | -108185.2598 | -144247.0131 | -180308.7663 | -216370.5196
EV | -49888.0973 | -99776.1947 | -149664.292 | -199552.3893 | -249440.4867 | -299328.584
NOX Reductions with % Change form Gasoline to Alternative Fuels |  |  |  |  |  | 
Fuel Tech | 5% | 10% | 15% | 20% | 25% | 30%
CNG | (8,181) | (16,363) | (24,544) | (32,725) | (40,906) | (49,088)
E85 | (17,239) | (34,478) | (51,716) | (68,955) | (86,194) | (103,433)
HEV | (36,062) | (72,124) | (108,185) | (144,247) | (180,309) | (216,371)
EV | (49,888) | (99,776) | (149,664) | (199,552) | (249,440) | (299,329)
Total Annual Pounds of NOX Emissions All passenger cars and trucks
San Patricio and Nueces Counties
973,676

## Slide 22
Chart: % Change from Conventional Fuel Passenger Vehicles to Alternative Fuels VOC Reductions
| 5% Change | 10% Change | 15% Change | 20% Change | 25% Change | 30% Change
CNG | -0.022557 | -0.045115 | -0.067672 | -0.09023 | -0.11279 | -0.13534
E85 | -0.0046904 | -0.0093807 | -0.014071 | -0.018761 | -0.023452 | -0.028142
HEV | -0.02564 | -0.051281 | -0.076921 | -0.10256 | -0.1282 | -0.15384
EV | -0.05 | -0.1 | -0.15 | -0.2 | -0.25 | -0.3

## Slide 23
Chart: Possible Annual Pounds of VOC Reduced With % Change from Gasoline to Alternative Fuels
| 5% Change | 10% Change | 15% Change | 20% Change | 25% Change | 30% Change
CNG | -20630.1492 | -41260.2985 | -61890.4477 | -82520.597 | -103150.7462 | -123780.8954
E85 | -4289.6307 | -8579.2615 | -12868.8922 | -17158.5229 | -21448.1536 | -25737.7844
HEV | -23449.7455 | -46899.491 | -70349.2364 | -93798.9819 | -117248.7274 | -140698.4729
EV | -46382.1485 | -92764.2969 | -139146.4454 | -185528.5938 | -231910.7423 | -278292.8907
VOC Reductions with % Change form Gasoline to Alternative Fuels |  |  |  |  |  | 
Fuel Tech | 5% | 10% | 15% | 20% | 25% | 30%
CNG | (20,630) | (41,260) | (61,890) | (82,521) | (103,151) | (123,781)
E85 | (4,290) | (8,579) | (12,869) | (17,159) | (21,448) | (25,738)
HEV | (23,450) | (46,899) | (70,349) | (93,799) | (117,249) | (140,698)
EV | (46,382) | (92,764) | (139,146) | (185,529) | (231,911) | (278,293)
Total Annual Pounds of VOC Emissions All passenger cars and trucks
San Patricio and Nueces Counties
914,562
VOC Reductions with % Change form Gasoline to Alternative Fuels |  |  |  |  |  | 
Fuel Tech | 5% | 10% | 15% | 20% | 25% | 30%
CNG | (20,630) | (41,260) | (61,890) | (82,521) | (103,151) | (123,781)
E85 | (4,290) | (8,579) | (12,869) | (17,159) | (21,448) | (25,738)
HEV | (23,450) | (46,899) | (70,349) | (93,799) | (117,249) | (140,698)
EV | (46,382) | (92,764) | (139,146) | (185,529) | (231,911) | (278,293)

## Slide 24: VW Offending Vehicles
Cars registered locally (.1% of local cars) 
NOX released above certified 
Exhaust equivalent of adding cars 
% of NOX from offending cars
10X to 40X
2-7 % of NOX from cars
313
2,817 to 12,207

## Slide 25: AFLEET Tool -Argonne National Laboratory

## Slide 26: Sources and Resources
AutoCheck.cc
http://www.afdc.energy.gov/
http://www.hybridcars.com/
https://greet.es.anl.gov/afleet
http://www.eia.gov/forecasts/aeo/tables_ref.cfm